## Slide 1
低资源开销Frodo总方案

## Slide 2
1
低资源开销策略
  控制模块采用二级译码策略
  Hash模块采用折叠结构
低资源消耗Frodo——整体架构设计
华中科技大学
Huazhong University of
Science and Technology
核心算子
  Hash(矩阵生成),MACs(矩阵乘加运算),Sampler(高斯采样),Controller(主控)

## Slide 3
2
二级译码
  算法—指令—微指令二级译码降低资源开销
  微程序修改方便，利于迭代
低资源消耗Frodo——设计细节
华中科技大学
Huazhong University of
Science and Technology
采用循环折叠的方法设计Hash
减少Keccak运算所需的LUT资源
    Slice为Keccak运算基本单位
    一轮Keccak处理200bit(8slice)
    重排Keccak24轮运算子步骤
    设计Dram集群与相关读写控制
控制模块架构图

## Slide 4
3
低资源消耗Frodo——结果对比
华中科技大学
Huazhong University of
Science and Technology
 | Keygen | Encap | Decap
FrodoKEM-640 |  |  | 
FrodoKEM-976 |  |  | 
FrodoKEM-1344 |  |  | 
运行周期数
经DC综合总逻辑门数为 ，符合要求
低资源开销 Frodo 硬件实现：
(2.1) 硬件实现等效逻辑门数小于等于 100 万
(2.2) 基于 PTPX 功耗分析工具，评估 16MHz/24MHz 频率下的芯片运行功耗
 | Keygen | Encaps | Decaps
Howe et al. [1] | 85,585,315 | 112,103,350 | 112,442,770
Bos et al. [2] | 81,299,689 | 86,255,368 | 87,212,153
Banerjee et al. [3] | 11,453,942 | 11,609,668 | 12,035,513
Dang et al. [4] | - | 1,186,704 | 1,309,884
Karl et al. [5] | 23,403,216 | 25,466,437 | 25,307,100
This work |  |  | 
FrodoKEM-640实现周期数对比
 | Platform | LUT | FFs | BRAMs | DSPs
Dang et al. [4]1 | UItraScale+ | 7,015 | 6,610 | 17.5 | 32
Karl et al. [5]2 | UltraScale+ | 5,590 | 1,118 | 0 | 2
This work | UltraScale+ |  |  |  | 
资源开销
[1]J. Howe, T. Oder, M. Krausz, and T. Gneysu, “Standard lattice-based key encapsulation on embedded devices,” IACR Transactions on Cryptographic Hardware and Embedded Systems, pp. 372–393, aug 2018.
[2]J. W. Bos, S. Friedberger, M. Martinoli, E. Oswald, and M. Stam, “Fly, you fool! Faster Frodo for the ARM Cortex-M4.” Cryptology ePrint Archive, Report 2018/1116, 2018.
[3]U. Banerjee, T. S. Ukyab, and A. P. Chandrakasan, “Sapphire: A Configurable Crypto-Processor for Post-Quantum Lattice-based Protocols,” IACR Transactions on Cryptographic Hardware and Embedded Systems, pp. 17–61, aug 2019.
[4]V. B. Dang, F. Farahmand, M. Andrzejczak, and K. Gaj, “Implementing and Benchmarking Three Lattice-Based Post-Quantum Cryptography Algorithms Using Software/Hardware Codesign,” in 2019 International Conference on Field-Programmable Technology (ICFPT), IEEE, dec 2019.
[5]P. Karl, T. Fritzmann, and G. Sigl, “Hardware Accelerated FrodoKEM on RISC-V,” in 2022 25th International Symposium on Design and Diagnostics of Electronic Circuits and Systems (DDECS), Apr. 2022, pp. 154–159.
低资源开销 Frodo 硬件实现：
(1) 硬件实现等效逻辑门数小于等于 100 万
(2) 基于 PTPX 功耗分析工具，评估 16MHz/24MHz 频率下的芯片运行功耗

## Slide 5
4
低资源消耗Frodo——进度安排
华中科技大学
Huazhong University of
Science and Technology
已完成工作
论文创新点
  设计了一种基于集群RAM的折叠Hash结构
  设计了一种算法—指令—微指令的二级译码控制架构，为后量子密码算法的低资源开销实现提供一种新的范式
    硬件代码编写
    单个指令功能仿真测试均已通过
    专利原稿
正在进行
    全流程功能仿真测试
    上板验证
    低资源开销Frodo论文
    硬件实现评估报告